792-9000 Rotating Track Gate

SECTION 11 68 33.43	Track and Field Equipment

PART 1	GENERAL

1.1		WORK INCLUDED

A.		Provide all equipment and materials, and do all work necessary to furnish

and install the athletic equipment, as indicated on the drawings and as

specified herein.  Athletic equipment shall include, but not be limited to:

1.  792-9000 Rotating Track Gate

2.  792-9004 Set of 4 (optional)

1.2		RELATED WORK

A.		Examine contract documents for requirements that affect work of this

section.  Other specification sections that directly relate to the work of

this section include, but are not limited to:

1.  Section 02200 – Earthwork; Excavation and Backfill and

establishment of sub-grade elevations.

2.  Section 02511 – Asphalt, Concrete, and Pavement

3.  Section 02535 – Synthetic Track Surfacing

4.  Section 02542 – Synthetic Field Surfacing

5.  Section 03300 – Cast-in-Place Concrete

1.3		REFERENCES

A.		Comply with applicable requirements of the following standards.  Where

these standards conflict with other specified requirements, the most

restrictive requirements shall govern.

1.  World Athletics (Formerly IAAF)

2.  National Collegiate Athletic Association (NCAA)

3.  National Federation of State High School Associations (NFHS)

4.  American Sports Builders Association (ASBA)

5.  Manufacturers Data and Recommended Installation

Requirements

1.4		SUBMITTALS

A.		Manufacturers Product Data

1.  Provide manufacturers product data prior to actual field

installation work, for Architects or Owners representatives

review.

B.		Shop Drawings

1.  Provide drawings of the manufacturers recommended

installation and foundation requirements prior to actual field

installation work, for Architects or Owners representatives

review.

1.5		QUALITY ASSURANCE

A.		Manufacturers warranties shall pass to the Owner and certification made

that the product materials meet all applicable grade trademarks or conform 		to industry standards and inspection requirements.

B. 	Single Source Responsibility: Provide equipment from single manufacturer

C.	Manufacturer’s Qualifications: Minimum of 7 consecutive years experience manufacturing items similar to that specified.

1.6		PRODUCT DELIVERY AND STORAGE

A.		Materials delivered to the site shall be examined for damage or defects in 			shipping.  Any defects shall be noted and reported to the Owners 				representative.  Replacements, if necessary, shall be immediately re-			ordered, so as to minimize any conflict with the construction schedule.  			Sound materials shall be stored above ground under protective cover or 			indoors so as to provide proper protection.

1.7 		WARRANTY

A.	Provide 3-year warranty against defects in materials and workmanship, unless otherwise specified

PART 2	PRODUCTS

2. 1		MANUFACTURERS

A. 	Acceptable Manufacturer: UCS, Inc. 511 Hoffman Road, Lincolnton, NC 28092, phone 800-526-4856, fax 704-732-9559, web address: www.ucsspirit.com

B. 	       Substitutions: Not Permitted

2.2		RoTATING TRack Gate

A. 		792-9000 Rotating Track Gate

1. Each gate is manufactured in 3 parts:

a. Beam is 4” x 2” aluminum with 1/8” thick wall

b. Upright is 5” x 2” aluminum with 1/8” thick wall

c. Support Brace is 5” x 2” aluminum

2. Ground Sleeve Included with 4” Inside Diameter

3. Sandblasted and Powder Coated Silver with 3” Lettering in Red

4. Welded external locking Device for key-lock or combo-lock available

(Lock not provided by UCS Inc)

5.  Set of 4 Gates = model 792-9004

# PART 3 	EXECUTION

3.1		INSTALLATION OF EQUIPMENT

A.  		All athletic equipment shall be installed as recommended with 				manufacturer's written directions, and as indicated on the drawings.

END OF SECTION